## Slide 1
Course Name: Digital image processing Lab
Course Code: CSE-5211
Project Title: Object Size Measurement Using Aruco Marker
What is Aruco Marker?
7 X 7
Application of Aruco Marker
Object size measurement
AR vision mapping
Robotic Control
Drone Navigation system
Distance Estimation
3D object mapping
How Aruco Marker Works
1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0
1st | 2nd | 3rd | 4th | 5th
Marker ID: 0011000000
ID in decimal: 192
How to measure the size of an object
Place an Object with aruco marker
Capture footage and detect marker
Compute centroid of marker along with known 2D location in the plane and compute homography
Detect the object and apply homography to get 2D plane coordinates
How marker detection algorithm works
Convert into gray
Test Image
Adaptive threshold
Find Contours
Find Rectangles
Find Valid markers
Calculate Markers ID
Team Member: MD. SHIHABUL KOBIR Reg.No.: 2017-14-15
HARUNAR RASHID Reg.No.: 2016-13-22
Object Size Measurement
Presented to : Md. Mynoddin, Assistant Professor, CSE, RMSTU